Department of Electronics Engineering,

Communication Systems Laboratory

Laboratory Manual

for

B. Tech. (Electronics), IV Year (VII – Semester)

Lab Course EL 491 ( Electronics Circuit Design Lab.)

LIST  OF  EXPERIMENTS

- Quadrature Oscillator

- Switch-Capacitor LPF

- OTA-based Multi-function filters

- Precision Rectifier using Bi-phase amplifier

- Opamp-based Multi-function filters

- All-pass characteristics of CFA

------------------------

Compiled by

M. Hadi Ali Khan

B. Sc. Engg (AMU)., Ex-MIEEE (USA), Ex-MIETE (India), Ex-MSSI (India)

Electronics Engineer,

Department of Electronics Engineering,

AMU, Aligarh – 202 002

Email:-  mhadialikhan@aol.in

Note:- This laboratory manual can also be downloaded from following website of the Comm Lab:- http://amucomlab.googlepages.com/index.html

Experiment 1

Object:  Design and experimentally verify a quadrature oscillator for given frequency  using OPAMP

Circuit Diagram:

Theory:  With simple and routine analysis following relations can be derived:

(1.1)

(1.2)

(1.3)

Design:  Select appropriate value of  and calculate  from

(1.4)

Now using (3) work out  by selecting appropriate value of

Report:  Plot waveforms at output and input and verify the designed frequency.  Also give your comments on results and carry out circuit analysis.

# Experiment 2

Object:  Design and experimentally verify a first order low pass switched capacitor (SC) filter with cutoff frequency .

Circuit Diagram:

Theory:

(2.1)

Using switches and  and capacitor , we can realize  as shown in figure and its value given as

(2.2)

Where  is the clock frequency of two non-overlapping pulses  and

Design:

(2.3)

Note:   should be chosen approximately 20-30 times higher than .  Use IC 7400 to realize  and  and IC 4066 to realize switches  and .

Report:  Plot frequency response of low pass filter and verify the designed cutoff frequency .  Also give your comments on results and carry out circuit analysis.

# Experiment 3

Object:  Design and verify the OTA-C based multifunction filter to realize lowpass, highpass, bandpass and band elimination responses for given cutoff frequency .

Circuit Diagram:

Theory:  The routine analysis yields the output  as

(3.1)

(3.2)

(3.3)

Design: Make  in expression of , which reduces to

(3.4)

Note:  Select  in 50-100(A for LM 3080 OTA.

Report:  Plot frequency response of each filter on same semi-log graph paper and verify the designed cutoff frequency .  Also give your comments on results and carry out circuit analysis.

# Experiment 4

Object:  Design and verify the bi-phase amplifier as (a) Half wave precision rectifier (b) Full wave precision rectifier.

Circuit Diagram:

Result:  Plot output waveform for Half & Full wave precision rectifiers.  Also give your comments on results and carry out circuit analysis.

# Experiment 5

Object:  Design and verify the OPAMP based multifunction filter to realize lowpass, highpass, bandpass and band elimination responses for given cutoff frequency .

Circuit Diagram:

Theory:  The routine analysis yields the output  as

(5.1)

(5.2)

(5.3)

Design : Expression for

(5.4)

Note: For 741 OPAMP select  in the range 0.4-1.5MHz.

Report:  Plot frequency response of each filter on same semi-log graph paper and verify the designed cutoff frequency .  Also give your comments on results and carry out circuit analysis.

El 491  (Electronics Circuit Design Laboratory)

Experiment No.  5  (CFA)

| Object:- | Design an all pass section using CFA (AD844) for a pole frequency ωp (= ωz) = 2 лfo (fo = gp-no KHz). Plot the frequency response of the designed AP section (magnitude and phase of Vo2 with respect to Vi , versus frequency). |
| --- | --- |

Circuit Diagram:-

Design Equations:-

,	   			----   ----   (1)

----    ----   (2)

The pole frequency ωp =  ωz  =  	----    ----   (3)

( R = 10 KΩ,  R1 = 22 KΩ )

(Vi = 0.4 Vp-p / 1.5 KHz Sine wave may be used for initial testing of the designed circuit).

## Ratings of AD844 (60 MHz, 2000 V/µs Monolithic Op Amp):-

Wide-range of Biasing Power Supplies:  4.5 V to  18 V; Capable of high o/p drive of 50 mA to50 Ω;

Low offset voltage: 150 µV; Low Quiescent current: 6.5 mA; Large BW :  60 MHz at Gain of -1;

# Text boxes

Full wave

Half wave

# Pin Connections:-