PLL as the FM Demodulator

| Object:- | (a) Determine the lock-range and the Capture-range of the given PLL kit. |
| --- | --- |
|  | (b) Plot the demodulation characteristics ( VD vs ∆f ) and verify that the given PLL circuit is working as the Demodulator. Of the FM signal. |

Apparatus Used :-	1. The PLL Kit,

2. A Function generator with digital frequency display (1 MHz)

3. A Dual Trace CRO (20 MHz)

Figure 1 shows the experimental set-up & fig. 2 shows the Block-diagram of a PLL chip

Theory :- The functional characteristics of the PLL are described in the Data-sheet supplied by the manufacturer of PLL chip NE565. Refer to the data-sheet of NE565.

Observations:-     (a)  Free-running frequency, fo = -------  KHz ;   (fo = 1/To,  )

f1 = ………………KHz ; 	( L  --  UL )

f2 = ……………    KHz ;	  	( UL  --  L )

f3 = ………………KHz ;		( L  --  UL )

f4 = ………………KHz ;		( UL  --  L )

(b)  Lock-range (fL)     =  ( f1 – f3)  =           KHz

(c)  Capture-range (fc) =  ( f2 – f4 )  =           KHz ;   (Verify that fL > fc  )

(d) Readings for Demodulation Characteristics:

| S. No. | Incoming signal frequency (fi) | DC Level of the Differential output (VD) | ∆f = ( fi – fo) |
| --- | --- | --- | --- |

Vi  =  a sinusoidal signal having variable frequency & amplitude around 8 volts p-p (obtained

from an external signal generator) to be connected at input of the PLL marked Vi ; for

the purpose of determination of the lock-range, capture-range & the Demodulation

characteristics of the PLL circuit.

Result:-

A curve between VD versus ∆f shows the Demodulation characteristics of the PLL and is linear, which justifies that the given circuit of the PLL (NE565) is working as a demodulator of a FM signal having maximum frequency deviation less than the lock-range of the PLL..

Report:-

- Draw the circuit diagram of the PLL and give an expression for its free-running frequency.

- Discuss the applications of the PLL in actual practice.

Circuit diagram of FM Demodulator using PLL NE565 / LM565

*************

# Text boxes

Figure 1

Figure 2